## Slide 1
Luke Canny 19339166 Supervisor: Dr Fearghal Morgan
Masters Electronic and Computer Engineering Co-assessor: Mr Liam Kilmartin
GitHub.com/HDLGen-ChatGPT/PYNQ-SoC-Builder
6
PYNQ Automated System-on-Chip Builder
& Remote RISC-V Learning Platform
Project Overview and Objectives
The aim of this project is to:
Create a remote PYNQ laboratory for students
Extend the functionality of HDLGen-ChatGPT to automatically deploy projects to PYNQ-Z2 FPGAs
Develop an interactive challenge-based RISC-V learning tool
Acknowledgements
I would like to thank Dr. Fearghal Morgan for his support and guidance, and Roshan George, JP Byrne and Abishek Bupathi for their previous work on HDLGen-ChatGPT, PYNQ and RISC-V.
Future Work
Automate RISC-V Core Bitstream Creation
Develop a range of RISC-V challenges of varying difficulty
Gather feedback from potential users of RV learning platform
PYNQ SoC Builder
HDLGen-ChatGPT is an open-source Python tool developed in the University of Galway to enable fast capture of HDL-based SoC capture and implementation, by automated VHDL/Verilog, testbench and waveform generation. PYNQ SoC Builder is a Python application which builds HDLGen-ChatGPT projects.
PYNQ SoC Builder completes the following:
Generates and imports PYNQ-Z2 constraints and configuration
Creates and populates a Vivado Block Design
Configures PYNQ board I/O Connections
Performs synthesis, implementation and bitstream generation
Generates a Jupyter Notebook project based on test plan
Remote PYNQ FPGA Laboratory
The purpose of the remote FPGA laboratory is to make real PYNQ Z2 hardware available to students and enthusiasts.
This is achieved by using a tunnelling service called ngrok. This service runs as a background daemon on the PYNQ’s ARM processor. Ngrok encrypts all data using HTTPS and authenticates users using OAuth 2.0. OAuth allows users to authenticate using their @universityofgalway.ie Microsoft accounts.
RISC-V Assembly/C Challenge-Based Learning Platform
Block Diagram generated by SoC Builder for a 4-bit Counter
PYNQ
SoC
Builder
Component Name, Description,
Date, Author,
Email, Company
Sub-Components
Signal Type
Sub-components
Ports
Internal Signals
Architecture
Test Plan
1. Read
Data
3. Invoke script in Vivado IDE
Output Binaries
.hwh, .tcl, .bit, .ipynb
2. Prepare a Tcl script which applies build steps in Vivado
4. Vivado exports binaries
5. Generate Jupyter NB based on Test plan
6. Export Binaries and JNB to output folder
7. User uploads
output to FPGA
HDLGen Project XML Data
RISC-V Architecture
Connection is tunnelled through ngrok servers
The purpose of the RISC-V learning platform through the remote laboratory is to encourage interaction and exploration of RISC-V ISA on real hardware, rather than simulation
The learning platform will consist of two RISC-V cores. One of which the user will program using assembly or C, The other will remain hidden, only visible to the core #1 by I/O ports. Core #2 will imitate a peripheral device.
The goal of the user is to interface with the hidden peripheral. The hidden peripheral changes depending on the difficulty level. For example, an interrupt controller or I2C device.
PYNQ Jupyter Notebook Interface
User uploads assembly to Core #1
Core #1
Core #2
Core #2 runs hidden program
User may read memory to view results
Project Workflow
Design Specification
User enters details
PYNQ SoC
Builder
Creates Vivado Tcl script with build steps, generates JNB file from HDLGen XML
HDLGen XML
Upload Binaries to remote/local FPGA
Run Overlay using Python in Jupyter Web Interface
Export Tcl and JNB
Generates FPGA Overlay from Tcl Build Steps
HDLGen-ChatGPT
Generates Vivado Project, Captures VHDL/Verilog, Generates Testbench
Context Diagram
Signal Dictionary
Process Descriptions
Data Flow Diagram
Truth Table etc.