## Slide 1
dIn1
dIn0
dOut
Mux2_1 Walkthrough – PYNQ & SoC Builder Basics
sel
dIn0 | dIn1 | sel | dOut
X | Y | 0 | X
X | Y | 1 | Y
Truth Table
dIn0 | dIn1 | sel | dOut
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 0
Test Plan
Component Symbol
Target Language: Verilog

## Slide 2
addIn1
dOut
2-bit Full Adder Walkthrough
Truth Table & Test plan
Component Symbol
Target Language: VHDL
addIn0
cOut
addIn1 | addIn0 | cIn | dOut | cOut
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1
cIn

## Slide 3
RISC-V ALU Walkthrough
Component Symbol
Target Language: VHDL
A
B
ALUOut
selALUOp
branch
32
32
32
4

## Slide 4
RISC-V ALU Walkthrough
Test plan
Signals | selALUOp | A | B | ALUOut | branch | Delay | TestNo | Note
Mode | in | in | in | out | out | None | None | None
Radix | 4'b | 32'h | 32'h | 32'h | 1'b | None | None | None
= | = | = | = | = | = | = | = | =
 | 0000 | 5a5a5a5a | 15a5a5a6 | 70000000 | 0 | 1 | 1 | sgnA + sgnB
 | 0000 | 15a5a5a6 | 5a5a5a5a | 70000000 | 0 | 1 | 2 | sgnA + sgnB
 | 0000 | ffffffff | 40000000 | 3fffffff | 0 | 1 | 3 | 
 | 0001 | ffffffff | fffffffe | 00000001 | 0 | 1 | 4 | sgnA - sgnB
 | 0010 | f0c3a596 | 1f7e8ab4 | 10428094 | 0 | 1 | 5 | A and B
 | 0011 | f0c3a596 | 1f7e8ab4 | ffffafb6 | 0 | 1 | 6 | A or B
 | 0100 | f0c3a596 | 1f7e8ab4 | efbd2f22 | 0 | 1 | 7 | A xor B
 | 0101 | f0c3a596 | 00000008 | c3a59600 | 0 | 1 | 8 | A << B(4:0) shift left logical
 | 0110 | f0c3a596 | 00000008 | 00f0c3a5 | 0 | 1 | 9 | A >> B(4:0) shift right logical
 | 0111 | f0c3a596 | 00000008 | fff0c3a5 | 0 | 1 | 10 | A >>> B(4:0) shift right arithmetic
 | 1000 | f0c3a596 | 1f7e8ab4 | 00000001 | 0 | 1 | 11 | 1 if sgn A < sgn B
 | 1001 | f0c3a596 | 1f7e8ab4 | 00000000 | 0 | 1 | 12 | 1 if uns A < uns B
 | 1010 | f0c3a596 | 1f7e8ab4 | 00000001 | 0 | 1 | 13 | branch = 1 if A = B
 | 1010 | f0c3a596 | f0c3a596 | 00000002 | 1 | 1 | 14 | branch = 1 if A = B
 | 1011 | f0c3a596 | 1f7e8ab4 | 00000003 | 1 | 1 | 15 | branch = 1 if A != B
 | 1011 | f0c3a596 | f0c3a596 | 00000004 | 0 | 1 | 16 | 
 | 1100 | f0c3a596 | 1f7e8ab4 | 00000005 | 1 | 1 | 17 | branch = 1 if sgn A < sgnB
 | 1100 | f0c3a596 | f0c3a596 | 00000006 | 0 | 1 | 18 | 
 | 1101 | f0c3a596 | 1f7e8ab4 | 00000007 | 0 | 1 | 19 | branch = 1 if sgn A >= sgnB
 | 1101 | f0c3a596 | f0c3a596 | 00000008 | 1 | 1 | 20 | 
 | 1110 | f0c3a596 | 1f7e8ab4 | 00000009 | 0 | 1 | 21 | branch = 1 if uns A < uns B
 | 1110 | f0c3a593 | f0c3a596 | 00000010 | 1 | 1 | 22 | 
 | 1111 | f0c3a596 | 1f7e8ab4 | 00000011 | 1 | 1 | 23 | branch = 1 if uns A >= uns B
 | 1111 | f0c3a596 | f0c3a596 | 00000012 | 1 | 1 | 24 | 

## Slide 5
dataIn(3:0)
count(3:0)
CB4CLED Walkthrough
Component Symbol
Target Language: VHDL
load
4-bit Cascadable, Chip-Enabled, Up/Down Synchronous Counter
with Asynchronous reset
up
ce
clk
rst
ceo
TC
load | loadDat | ce | up | count | TC | ceo | Delay
1 | d | 0 | 0 | D | 0 | 0 | 1
0 | d | 1 | 1 | F | 1 | 1 | 2
0 | d | 0 | 1 | F | 1 | 0 | 1
0 | d | 1 | 1 | 1 | 0 | 0 | 2
0 | d | 1 | 0 | 0 | 1 | 1 | 1
0 | d | 0 | 0 | 0 | 1 | 0 | 1
0 | d | 1 | 0 | F | 0 | 0 | 1
0 | d | 1 | 0 | 0 | 1 | 1 | 15
Test plan

## Slide 6
CB4CLED Walkthrough
4-bit Cascadable, Chip-Enabled, Up/Down Synchronous Counter
with Asynchronous reset
Signals load loadDat ce up count TC ceo Delay TestNo Note
Mode in in in in out out out None None None
Radix 1'b 4'h 1'b 1'b 4'h 1'b 1'b None None None
= = = = = = = = = = =
1 d 0 0 d 0 0 1 1 load 0xd
0 d 1 1 f 1 1 2 2 0xf, TC and ceo asserted
0 d 0 1 f 1 0 1 3 0xf, TC asserted, ceo deasserted
0 d 1 1 1 0 0 2 4 count increments to 0, ,then to 1
0 d 1 0 0 1 1 1 5 count down to 0, TC and ceo asserted
0 d 0 0 0 1 0 1 6 0, TC asserted, ceo deasserted
0 d 1 0 f 0 0 1 7 count own to 0xf
0 d 1 0 0 1 1 15 8 0, TC and ceo asserted
# Example of a comment - comments are ignored by the testplan generator
# HDLGen-ChatGPT Test Specification
# Title: 4-bit cascadable, loadable, up/down counter, with asynchronpous rst
# Created by: Fearghal Morgan
# Date: 20/02/2024
# Component type: Register-Transfer Logic

## Slide 7
sw
aShot
Single Shot Walkthrough
Timing Diagram
Component Symbol
Target Language: VHDL
clk
rst

## Slide 8
sw
aShot
Single Shot Walkthrough
Timing Diagram
Component Symbol
Target Language: VHDL
clk
rst

## Slide 9
RWr
rs1D(4:0)
RISC-V Register Bank Walkthrough
Component Symbol
Target Language: VHDL
rd(4:0)
rs1(4:0)
rs2(4:0)
clk
WBDat(31:0)
ce
rst
host_datToMem(31:0)
host_memAdd(15:0)
RBWe
WBDat(31:0)
rs2D(4:0)
RBOut(31:0)

## Slide 10
External Ports
RISC-V ALU
AXI GPIO
IP Blocks
AXI Interconnect
ZYNQ Processing System
Processor System Reset

## Slide 11
External Ports
RISC-V
Register Bank
AXI GPIO
IP Blocks
AXI Interconnect
ZYNQ Processing System
Processor System Reset

## Slide 12
Input AXI GPIO IP Blocks
Mux2_1
Output AXI GPIO IP Blocks
AXI Interconnect
ZYNQ Processing System
Processor System Reset

## Slide 13
AXI GPIO IP Blocks
Mux2_1
AXI Interconnect
ZYNQ Processing System
Processor System Reset

## Slide 14
Path to Vivado Bat File
Instructs Vivado to operate in Tcl Console Mode
Source command in Tcl is used to execute Tcl scripts
Path to Tcl script with build instructions